Difference between router and switch

In those early days when router is router and switch is switch, these two are different in several ways:

- Router understand IP head, and switch deal with MAC address

- Router has its own IP address(es), and switch don’t

- Router has an operating system running inside, and allow administrator to login into the system.

- You (network administrator) must configure routing table to make it works.

- Switch is usually ready to use.

- Router has routing software running inside, including route discovery protocol.

- Routing software know how to deal with different IP packet, such as ICMP and other IP option functionality. Switches don’t.

- Multiple routers can be connected together as a network.

- You can’t directly multiple switches together to form a large network.

| Router | Switch |
| --- | --- |
| Technical Specifications: | Routers operate at Layer 3 (Network) of the OSI model. | Network switches operate at layer two (Data Link Layer) of the OSI model. |
| Layer: | Network Layer (Layer 3 devices) | Data Link Layer (Layer 2 devices) |
| Table: | Store IP address in Routing table and maintain address at its own. | Store MAC address in lookup table and maintain address at its own, Switch can Learn MAC address. |
| Used in (LAN/MAN/WAN): | LAN . WAN | LAN |
| Collision: | Less | In Full Duplex Switch no Collision occur. |
| Ports: | 2/4/8 | Switch is multi port Bridge. 24/48 ports |
| Device Type: | Networking device | Active Device (With Software) & Networking device |
| Data Transmission form: | Packet | Frame (L2 Switch) Frame & Packet (L3 switch) |
| Bandwidth sharing: | Bandwidth sharing is Dynamic (Enables either static or dynamic bandwidth sharing for modular cable interfaces. The default percent-value is 0. The percent-value range is 1-96.) | If speed of switch is 10/100 Mbps then bandwidth of each and every one of its ports gets 10/100 Mbps. |
| Broadcast Domain: | In Router, every port has its ownBroadcast domain. | Switch has one broadcast domain[unless VLAN implemented] |
| Speed: | 1-10 Mbps(Wireless) 100 Mbps (Wired) | 10/100Mbps, 1Gbps |
| Routing Decision: | Take faster Routing Decision | Take more time for complicated routing Decision |
| NAT (Network Address Translation): | Can Perform NAT | Switches can Not perform NAT |
| Faster: | In a different network environment (MAN/ WAN) Router is faster than L3 Switch. | In a LAN environment L3 switch is faster than Router (built in switchning hardware) |
| Features: | Firewall VPN Dynamic hadling of Bandwidth | Priority rt range On/Off setting of port VLAN Port mirroring |
| Latest Models: | Linksys WRT54GL Juniper MX & EX series Cisco 3900,2900,1900 | Alcatel's OmniSwitch 9000; Cisco Catalyst switch 4500 and 6500(10 Gbps), |